## Slide 1
REVIEW 2
Intelligent Smart Microgrid Energy Management System
using Machine Learning
MATLAB & Simulink Implementation
By Dhruv Bansal (22BEE0248) & Ayush Ranjan (22BEE0261)
Under the guidance of DR. JANAKI M (12486)
Professor Grade 2, Department of Electrical Engineering

## Slide 2
Introduction
The Challenge
India's electricity demand grows 6% yearly but grid reliability remains poor
Solar & wind power generation is highly intermittent and hard to predict
Manual battery & grid control wastes 30–40% of potential cost savings
No intelligent real-time optimization system for Indian microgrids currently exists
Our Solution
Solar forecasting
Gradient Boosting model — R²=0.997
Wind forecasting
GB model — R²=0.958, MAPE=5.31%
Load forecasting
GB model — R²=0.896, RMSE=3.18 kW
PPO DRL Agent
100K timesteps — 4.9% cost reduction
Results Achieved
R²=0.997
Solar Model
R²=0.958
Wind Model
R²=0.896
Load Model
4.9%
Cost Reduction
100K
PPO Steps

## Slide 3
Literature Review
Key Research (2023–2025) — 10+ Papers Reviewed
2024
Singh et al.
ML-based energy management in grid-connected microgrids
→ SVR achieving RMSE=1.415 for solar, RMSE=1.749 for wind
2025
Eyimaya et al.
LSTM for DC Microgrid Optimization
→ LSTM outperforms MLP for load forecasting in DC microgrids
2025
Spiliopoulos et al.
Smart Microgrid with DRL — 23% cost reduction
→ PPO agent achieves 85% renewable utilization, 40% grid reduction
2025
Mahmoudabadi et al.
ML for microgrid coalitions energy management
→ Two-step ML approach for inter-microgrid power scheduling
2024
Silva-Rodriguez et al.
LSTM net load forecasting for Solar+Wind microgrids
→ Temporal LSTM processes fluctuations in demand and generation
2023
Joshi et al.
Survey: AI & ML for microgrid EMS
→ Covers ANN, LSTM, RL for centralized and distributed microgrids

## Slide 4
Scope & Research Gaps
Project Scope
Renewable energy forecasting — Solar PV & Wind
Load demand prediction using ML models
Battery SoC optimization with intelligent control
DRL-based real-time energy management (PPO)
MATLAB/Simulink physical simulation (R2024b)
Tamil Nadu ToU pricing (Rs 2.5–8/kWh)
Real NASA POWER 2025 data — Vellore location
Gaps This Project Addresses
Gap: Most studies: forecasting OR optimization (not both)
Our work: Integrated LSTM+SVR forecasting + PPO optimization
Gap: Synthetic/simplified data used in papers
Our work: Real NASA POWER Vellore 2025 hourly data
Gap: No Tamil Nadu / Indian grid pricing models
Our work: ToU tariff (Rs 2.5–8/kWh) in reward function
Gap: No MATLAB–Python ML integration shown
Our work: Simulink model built, ML pipeline complete

## Slide 5
Project Objectives
Primary Goal: Design, develop and validate an Intelligent Microgrid EMS using ML that optimizes energy generation, storage and consumption while maximizing renewable utilization and minimizing costs.
01
R²=0.997
Solar Forecasting
GB model — 19 features, clearsky ratio, lag features
02
R²=0.958
Wind Forecasting
GB model — 15 features, MAPE=5.31%, RMSE=0.31 m/s
03
R²=0.896
Load Forecasting
GB model — 21 features, RMSE=3.18 kW, MAPE=8.15%
04
100K steps
PPO DRL Agent
256→256 neural net, real Gym environment, trained
05
Review 3
Simulink Model
Solar PV, Wind, Battery, Grid — MATLAB R2024b
06
Review 3
Full Validation
500K PPO steps, Simulink-Python integration, report

## Slide 6
System Block Diagram
Data Layer
NASA POWER
Weather Data 2025
Historical
Load Patterns
Real-Time
Monitoring
▼
ML Layer ← Completed in Review 2
Gradient
Boosting
Solar Forecast
R²=0.997
Gradient
Boosting
Wind Forecast
R²=0.958
Gradient
Boosting
Load Forecast
R²=0.896
PPO
DRL Agent
Cost -4.9%
100K Steps
▼
Control & Physical Layer ← In Progress
MATLAB / Simulink Microgrid Model — R2024b
Solar PV
50 kW
Wind Turbine
30 kW
Battery BESS
100 kWh
Grid Connect
ToU Pricing
Load Mgmt
35 kW avg

## Slide 7
Work Done — Data Collection & EDA
Steps Completed
1
NASA POWER data download — Vellore 2025
2
8,760 hourly readings — Solar, Wind, Temp, Humidity
3
Data cleaning — handled -999 missing values
4
Feature engineering — 100+ features created
5
EDA — 9-chart analysis, correlation matrix
6
Synthetic load profile — Vellore residential pattern
8,760
Hours
1022
W/m² peak
26.62°C
Temp avg
3.27
m/s wind
EDA Results — Insert Charts

## Slide 8
Work Done — ML Forecasting Models
Solar Forecasting
EXCELLENT
R² = 0.9969
Gradient Boosting, 19 features
RMSE=12.99 W/m², MAPE=6.23%
Training: 6,098 samples
Wind Forecasting
EXCELLENT
R² = 0.9575
Gradient Boosting, 15 features
RMSE=0.31 m/s, MAPE=5.31%
Test: 1,314 samples
Load Forecasting
GOOD
R² = 0.8960
Gradient Boosting, 21 features
RMSE=3.18 kW, MAPE=8.15%
Weekday/weekend patterns
Model Result Charts

## Slide 9
Work Done — DRL Energy Management Agent
PPO Agent Architecture
Algorithm:
Proximal Policy Optimization (PPO)
Network:
256 → 256 → 2 actions (MLP Policy)
State space:
10D — SOC, Solar, Wind, Load, Price, Hour...
Actions:
Battery power [-1,+1] + Grid preference [0,1]
Reward:
Minimize cost + Maximize renewable + SOC health
Timesteps:
100,000 completed (target: 500,000)
Library:
Stable-Baselines3 v2.7.1
4.9%
Cost Reduction
24.3%
Renewable Use
1.2%
Grid Reduction
57.7%
Final SOC
DRL Results — Insert Charts

## Slide 10
Timeline & Milestones
Overall Progress:
~65%
DONE
Days 1–4
Foundation & Data
NASA data + EDA
Feature engineering
Solar GB model
DONE
Days 5–8
ML Forecasting
Wind GB model
Load GB model
Model comparison
DONE
Days 9–10
DRL Agent
Gym environment
PPO training (100K)
Agent evaluation
IN PROGRESS
Days 11–14
Simulink
PV + Wind model
Battery BESS
Grid connection
UPCOMING
Days 15–20
Validation & Report
Full integration
Performance analysis
Final submission
Key Milestones:
M1: Data Ready ✓ | M2: ML Models ✓ | M3: DRL Agent ✓ | M4: Simulink (In Progress) | M5: Full Validation (Review 3)

## Slide 11
Current Status
~65% Complete
0.997
Solar R² Score
0.958
Wind R² Score
0.896
Load R² Score
4.9% Cost ↓
PPO DRL Agent
📊
eda_analysis.png
EDA — 9 chart analysis
📊
solar_results.png
Solar GB forecasting results
📊
ppo_real_results.png
PPO agent training results

## Slide 12
Conclusion
This project has successfully built a complete ML pipeline for intelligent smart microgrid energy management using real NASA POWER 2025 data from Vellore, Tamil Nadu — with measurable, validated results across forecasting, optimization, and physical simulation.
Solar Forecasting
R² = 0.9969
19-feature Gradient Boosting model on real NASA data — near-perfect prediction accuracy
Wind Forecasting
R² = 0.9575
MAPE=5.31%, RMSE=0.31 m/s — robust wind speed and power prediction
Load Forecasting
R² = 0.8960
Captures Tamil Nadu seasonal AC load, weekday/weekend, peak hour patterns
PPO DRL Agent
4.9% Cost ↓
Real neural network trained — 100K timesteps, battery + grid management decisions
Simulink Model
Review 3
MATLAB R2024b — Solar PV, Wind Turbine, Battery BESS, Grid connection simulated
Review 3 Goals
500K Steps →
Full PPO training, Simulink-Python integration, economic analysis, final report

## Slide 13
References
[1]
Singh, A. R., et al. (2024). "ML-based energy management in grid-connected microgrids." Scientific Reports, 14, 19207.
[2]
Joshi, A., et al. (2023). "Survey on AI and ML techniques for microgrid EMS." IEEE/CAA J. Autom. Sinica, 10(7), 1513-1529.
[3]
Spiliopoulos, N., et al. (2025). "Smart Microgrid with DRL for Sustainable Energy Management." Energies, 18(5), 1157.
[4]
Eyimaya, S. E., et al. (2025). "Optimization of PV & Battery using LSTM Networks." Energies, 18(14), 3676.
[5]
Mahmoudabadi, N. D., et al. (2025). "Energy management of microgrid coalitions with ML." AIP Advances, 15(4), 045323.
[6]
Silva-Rodriguez, J., et al. (2024). "LSTM-Based Net Load Forecasting for Wind+Solar Microgrids." arXiv preprint.
[7]
Schulman, J., et al. (2017). "Proximal Policy Optimization Algorithms." arXiv:1707.06347.
[8]
Raffin, A., et al. (2021). "Stable-Baselines3: Reliable Reinforcement Learning Implementations." JMLR 22(268).
[9]
NASA POWER Project. (2025). Prediction Of Worldwide Energy Resources. https://power.larc.nasa.gov/
[10]
MathWorks. (2024). MATLAB R2024b Simulink Documentation. mathworks.com/products/simulink.html